Retro_6809 Design Document – 6 July 2023

This project is to be an emulated 6809 processor based micro-computer to be developed around a pair of Raspberry PI PICO micro-controllers and a 64k QSPI static RAM chip as an external video buffer. Other chips may be needed to implement USB for mouse, keyboard, and game controllers. Because the older retro style audio chips are no longer in production, FM audio synthesis will be emulated via one of the PICO cores. Graphics will also be emulated using another core. This is to be kind of a “What if?” 80’s style retro computer.

Two Raspberry PI PICO micro-controllers will be used. Each of which has two M0 cores, 260mb RAM, and 2gb flash storage. PICO one, codenamed “TONI”, will drive the 6809 emulation (and 64k mapped memory) and video emulation with its two cores. PICO two, codenamed “KIMI”, will drive both FM synthesis and sampled sound as well as the main event dispatch unit for input and output. A single serial (QSPI) static RAM chip will act as a video buffer for the graphics display modes (or TONI’s graphics buffer).

Text modes will use a short block of internal memory (TONI) for its display buffer. Graphics modes will use the external serial RAM for its buffer. Simple sprite and tile graphics may be implemented in future versions.

TONI:
Core One – 6809 emulation and 64k mapped memory.
This includes implementation of all of the “hardware”
registers within the 6809 addressable memory.

Core Two – Video implementation. This core will render the
text display modes from a block of TONI’s memory, but
will also display the graphics modes that use the
external 64k static memory chip as a buffer. Pixel based
display modes will always display behind the last selected
text modes. Text will be overlayed with alpha transparency.
Sprites and/or tiles may be implemented in the future using
the external ram chip or TONI’s graphics buffer.

KIMI:
Core One – Event dispatch. This core will handle the
dispatching of input/output events such as: Keyboard,
mouse, game-pads, serial ports, GPIO via two USB ports
and/or SPI, QSPI, UART or parallel pins (GPIO).

Core Two – Audio. This core supports both emulated FM
synthesis as well as 8-bit DAC (digital to audio).

64K External Graphics Buffer RAM:
This will act as a place to store 256 Hardware Image Blocks	(HIBs). HIBs are simple 16x16 pixel 256 color image blocks that	can be used as tiles and/or sprites.
Video Modes:
There will be seven Tile graphics modes that can act as a background for the 15 text or pixel bitmap modes. While text or graphics can be layered in front of tiled modes, text and pixel bitmap modes share the same buffer and can therefore not be displayed simultaneously.

Sprites and Tiles (Hardware Image Blocks):
Hardware Image Blocks (HIBs) are simple 256-color 16x16 pixel images. They can be rendered either as tiles or sprites. There are loaded and cached within the 64k external memory buffer. There is room for 256 HIBs to be used as tiles and/or sprites.

Tiles are mapped from buffer from a block of CPU memory. If text/graphics are not used, the 5k text buffer may be used for a tile-map buffer. Sprites are to be rendered from a sprite lookup table placed within valid CPU accessible memory.

Graphics Mode Control Registers:

DSP_GMODE (byte read/write): xxAAA.BBBB
x = reserved bit
A = Tile Graphics Modes
A:0 Disable Tile Graphics	A:4 Tile 512x160 (32x10)
A:1 Tile 512x320 (32x20)	A:5 Tile 256x320 (16x20)
A:2 Tile 256x160 (16x10)	A:6 Tile 256x80 (16x5)
A:3 Tile 128x80 (8x5)	A:7 Tile 128x160 (8x10)
BB = Text/Pixel Bitmap Modes
B:0 Disable Text/Pixel Gfx	B:8 Pixel 256x160 1-bpp
B:1 Text 64x40 (512x320)	B:9 Pixel 256x80 1-bpp
B:2 Text 64x20 (512x160)	B:10 Pixel 256x80 2-bpp
B:3 Text 32x40 (256x320)	B:11 Pixel 128x160 1-bpp
B:4 Text 32x20 (256x160)	B:12 Pixel 128x160 2-bpp
B:5 Text 32x10 (256x80)	B:13 Pixel 128x80 1-bpp
B:6 Text 16x20 (128x160)	B:14 Pixel 128x80 2-bpp
B:7 Text 16x10 (128x80)	B:15 Pixel 128x80 4-bpp

DSP_FLAGS (byte read/write): ABxx.xCCC
A = 1:WINDOWED, 0:FULLSCREEN
B = 1:VSYNC, 0:non-VSYNC
C = 0-7 display monitor to use

DSP_PAL_INDEX (read/write): AAAA.AAAA
A = Color palette access index. Write to DSP_PAL_COLOR prior to	accessing the color data in DSP_PAL_COLOR.

DSP_PAL_COLOR (word read/write): RRGG.BBAA [DSP_PAL_INDEX]
R = 4-bits of red color data
G = 4-bits of green color data
B = 4-bits of blue color data
A = 4-bits of alpha transparency data

DSP_GLYPH_IDX (Byte read/write): Text Glyph Index
Set this register to index a specific text glyph. Set this	value prior to updating glyph pixel data.

DSP_GLYPH_DATA (8-Bytes read/write): Text Glyph Pixel Data
Each 8x8 text glyph is composed of 8 bytes. The first byte in	this array represents the top line of 8 pixels. Each array entry	represents a row of 8 pixels.

DSP_HIB_IDX (Byte read/write): Hardware Image Block Index
Index within the HIB array. Set this register to index a	specific HIB. Set this value prior to updating tile/sprite image	data.

DSP_HIB_DATA (256-Bytes read/write): HIB Image Data
Contains a 256-byte long block that describes a 16x16 pixel	(256-color) image as indexed by DSP_HIB_IDX.

DSP_TILE_BUFFER (Word read/write): Start of the tile map buffer

DSP_TILE_WIDTH (Word read/write): Width (in tiles) of the tile-map

DSP_TILE_HEIGHT (Word read/write): Height (in tiles) of the tile-map

DSP_TILE_OFFSET (byte read/write): AAAA.BBBB
A = 0-16 negative horizontal pixel offset of the displayed tiles
B = 0-16 negative vertical pixel offset of the displayed tiles

DSP_GFX_START (Word read/write): Start address of text/pixel graphics
Defaults to the start of the standard graphics buffer. Can be	changed so long as the display fits within the graphics buffer.	This address will be clamped to min and max values based on	display requirements.

DSP_GFX_END (Word read only): Last address of text/pixel graphics
The system will set this value based on the value set within	DSP_GFX_START plus the buffer size required for the current	display.
Emulation Class Object Hierarchy:
Bus	the main loop contains all of the device objects
Device	the base/parent device object
CPU6809	the 6809 emulation layer
Memory	the memory container system
MEM	the parent memory node object
RAM	random access memory (read/write)
ROM	read only memory (read only)
REG	hardware register
Gfx	the graphics container
GfxMode	The graphics mode parent object
GfxPixel	pixel graphics display modes
GfxText	text glyph display modes
GfxCursor	mouse cursor (possibly utilizes GfxSprite)
GfxDebug	a basic debug monitor overlay
GfxTile	the tile graphics modes
GfxSprite	the sprite system
Keyboard	basic keyboard operation
GamePad	gamepad and joystick implementation
Mouse	mouse implementation
Audio	the audio container
AudioMode	The audio mode parent object
AudioDAC	digital to analog audio device (WAV)
AudioFM	frequency modulated audio emulation
GPIO	general input/output pins (parallel)
UART	for headless use/communication
Math	implements random and floating point functions
Timers	implements various hardware timers
FileIO	the file input and output Operating System

Bus
The Bus object acts as a container to dispatch events to all of the
attached devices. After it starts the CPU6809 and Audio threads, it
the main application loop and is responsible for proper device
shutdown as it exits.

Device::
Within the emulation, the Bus object acts as the main device
container, the main loop, and the main event dispatcher. Every device
should inherit from the Device object. The Device object should have
the following virtual members:
OnAttach()	called on creation to add to memory map
OnInit()	calls once after all devices are added
OnQuit()	called when Gfx is closed
OnActivate()	called when opening a new graphics mode
OnDeactivate()	called to close current graphics mode
OnEvent(event)	called when an event was received
OnUpdate(elapsedTime)	called every
OnRender()	called every frame for rendering images

Device::CPU6809
While the 6809 micro-processor will be initially implemented, it	will be possible to implement the Hitachi 6309 in the future by	adding those instructions to the CPU6809 object. In addition to the
inherited member functions, this object should include:
OnClock()	called every clock pulse in its own thread
OnReset()	initiates a reset
OnIRQ()	requests a standard interrupt
OnNMI()	requests a non-maskable interrupt
OnFIRQ()	requests a fast interrupt (video blanking)

Device::Memory	// This is a work in progress
This object handles the memory map and the hardware registers. It	acts as a Memory Node container. In addition to the inherited	members, it should include:
AttachDevice(device, data)	appends device hardware registers
ReadByte(addr, flag)	reads a byte from the memory map
WriteByte(addr, byte)	writes a byte to the memory map
ReadWord(addr, flag)	reads a word from the memory map
WriteWord(addr, word)	writes a word to the memory map
MEM::	the parent memory node object
MEM::RAM	random access memory (read/write)
MEM::	ROM	read only memory (read only)
MEM::	REG	hardware register

Device::Gfx
This object is a container for all of the graphics mode objects. It
receives events from the bus and dispatches them to the GfxMode
objects.

GfxMode::
Defines the parent Graphics Mode object. It implements the following
virtual functions:
OnAttach()	called on creation to add to memory map
OnInit()	calls once after all devices are added
OnQuit()	called when Gfx is closed
OnActivate()	called when opening a new graphics mode
OnDeactivate()	called to close current graphics mode
OnEvent(event)	called when an event was received
OnUpdate(elapsedTime)	called every frame counting elapsed time
OnRender()	called every frame for rendering images

GfxMode::GfxPixel
Implements the pixel graphics modes.

GfxMode::GfxText
Implements the text glyph modes.

GfxMode::GfxCursor
Implements the system cursor. This should also add registers to
customize said cursor. Simply displays a cursor icon at the position	described within the Device::Mouse hardware registers.
GfxMode::GfxDebug
This mode is a simple debug monitor overlay. It should include hex
dumps from multiple addresses that can be modified. It should display
and allow for editing of the registers. It should display a
disassembly of code in memory. Simple assembly functions could also
be implemented. RESET, IRQ, FIRQ, and NMI buttons should also be
present.

GfxMode::GfxTile
This will initially be in a skeleton form. Eventually this class
should implement the tile graphics modes.

GfxMode::GfxSprite
This will initially be in a skeleton form. Eventually this class
should implement the tile graphics modes.

Device::Keyboard
This object dispatches Keyboard events to the Bus for event
distribution. Updates its attached hardware registers.

Device::GamePad
This device object dispatches events from attached gamepads and/or	joysticks to the Bus for event distribution. Updates its own attached	hardware registers.

Device::Mouse
Implements mouse function within its own attached hardware registers.
Dispatches mouse events via the Bus Object.

Device::Audio
Acts as a container for attached AudioMode objects.

AudioMode::
The parent AudioMode object.

AudioMode::AudioDAC
This audio mode object handles two 8-bit digital to analog audio	ports. It should implement simple write to left/right DAC function	directly via hardware register ports. It should also handle clearing,
loading, volume, starting and stopping of WAV files.

AudioMode::AudioFM
This should implement one of the more popular 80’s era FM syntesis
chips. It would be cool to emulate the Commodore 64’s SID chip. Check
it out.

Device::GPIO
Read and/or Write to/from pins. This should dispatch events to the	Bus.

Device::UART
This should implement headless USB/Serial communications to/from	another RETRO_6809 computer or a host Linux/Windows machine.
Device::Math
Includes various 16 and 32 bit floating point operations with	corresponding float to integer conversions. Should implement all of	the most useful half and double precision floating point operations.	Also included in this object should include 16 bit random on read and	the ability to set the random seed on write.

Device::Timers
This should implement registers to read the date, and a 32-bit	“milliseconds since start” counter.
TIMER_DAY	(byte) day of the month (1-31)
TIMER_MONTH	(byte) month (1-12)
TIMER_YEAR	(word) year (0-65535)
TIMER_MS	(dword) number of milliseconds since start

Device::FileIO
This should cover all of the functionality a basic file operating	system should include. Things like, not not limited to, “dir”, “cd”,
“load”, “exec”, etc… should all be covered.

Basic Memory Map:

$0000-$00FF	(256 bytes)	Zero Page: system vectors and variables
$0100-$01FF	(256 bytes)	User Page: low memory user space/stack
$0200-$03FF	(512 bytes)	system stack
$0400-$17FF	(5K bytes)	text display buffer
$1800-$18FF	(256 bytes)	input/output buffer
$1900-$1FFF	(1.75K bytes)	system hardware registers
$2000-$CFFF	(44K bytes)	user RAM space
$D000-$EFFF	(8K bytes)	* paged memory
$F000-$FFEF	(4k bytes)	System KERNEL ROM
$FFF0-$FFFF	(10 bytes)	system hardware vectors

Paged Memory Notes:
bank 0: is simply 8K of fast RAM usable by the system (default)
bank 1: contains the directory structure for persistent memory
banks 2-255: contains 8K pages of persistent memory from 1MB of flash

Bank 0 is always just a 8K bank of fast memory that is usable by the	system for extra RAM for a total of 52K. It can be switched out to	any of the 253 banks	of persistent memory (from TONI’s flash). Bank 1	acts as an allocation	table accessed by ID. That ID is assigned via	the	Kernel. A program can request access to a page of persistent	memory via an assigned ID but it should release that ID when it’s	done using it. This should work similar to new or malloc but	requesting a full 8K page at a time. After use it should be deleted	or freed.

A low level read/write to the memory bank access register can bypass
the allocation function of the KERNEL for direct access. In this case	bank 1 would then be accessible by the program until the KERNEL is	used to once again access the TOC in bank 1 for allocation/releasing.