Retro_6809 Design Document – 6 July 2023

This project is to be an emulated 6809 processor based micro-computer to be developed around a pair of Raspberry PI PICO micro-controllers and a 64k QSPI static RAM chip as an external video buffer. Other chips may be needed to implement USB for mouse, keyboard, and game controllers. Because the older retro style audio chips are no longer in production, FM audio synthesis will be emulated via one of the PICO cores. Graphics will also be emulated using another core. This is to be kind of a “What if?” 80’s style retro computer.

Two Raspberry PI PICO micro-controllers will be used. Each of which has two M0 cores, 260mb RAM, and 2gb flash storage. PICO one, codenamed “TONI”, will drive the 6809 emulation (and 64k mapped memory) and video emulation with its two cores. PICO two, codenamed “KIMI”, will drive both FM synthesis and sampled sound as well as the main event dispatch unit for input and output. A single serial (QSPI) static RAM chip will act as a video buffer for the graphics display modes (or TONI’s graphics buffer).

Text modes will use a short block of internal memory (TONI) for its display buffer. Graphics modes will use the external serial RAM for its buffer. Simple sprite and tile graphics may be implemented in future versions.

TONI:
Core One – 6809 emulation and 64k mapped memory.
This includes implementation of all of the “hardware”
registers within the 6809 addressable memory.

Core Two – Video implementation. This core will render the
text display modes from a block of TONI’s memory, but
will also display the graphics modes that use the
external 64k static memory chip as a buffer. Pixel based
display modes will always display behind the last selected
text modes. Text will be overlayed with alpha transparency.
Sprites and/or tiles may be implemented in the future using
the external ram chip or TONI’s graphics buffer.

KIMI:
Core One – Event dispatch. This core will handle the
dispatching of input/output events such as: Keyboard,
mouse, game-pads, serial ports, GPIO via two USB ports
and/or SPI, QSPI, UART or parallel pins (GPIO).

Core Two – Audio. This core supports both emulated FM
synthesis as well as 8-bit DAC (digital to audio).

64K External Graphics Buffer RAM:
This will be a buffer for an additional block of memory to	handle pixel graphics, sprites, and/or 16x16 tile graphics. This	will be implemented along side the CPU mappable memory buffer on	Toni’s first core. This will be segmented into 160 byte blocks.
Video Modes:
There will be 8 total text modes and 8 total graphics modes all of which will be in a 16:10 aspect ratio with a 640x400 video timing. Text glyphs will be displayed from a 4k CPU mapped buffer and the pixel graphics will be displayed using 64,000 bytes of a 64k external graphics buffer. Both text and pixel graphics will be activated via their respective enable bits. The remaining 1.5k of extended memory will serve to house the dynamic graphics memory allocation table with up to 200 (7-byte) entries. The remaining 136 bytes will be reserved for future system use. Text and pixel graphics modes will each be selected via their own set of Graphics Mode Control Registers.

It will be possible to display text, graphics, or both at the same time. The text colors will be rendered from the first 16 colors within the 256 color palette. Text and graphics modes can be displayed simultaneously depending on the alpha component of the first 16 colors. If enabled, text will be displayed as a layer in front of the graphics layer. If the graphics layer is disabled, the background will be cleared to the color at index 0 within the color palette. Pixel graphics will only appear in the background layer if that layer is enabled.

Sprites and Tiles (Hardware Image Blocks):
Hardware Image Blocks (HIB) are simple 16 color 16x16 pixel images. The can be rendered as independently movable sprites or as tiles that are rendered as part of a map. An example of a sprite might be the mouse arrow cursor pointer. Each HIB is 160 bytes in length, 128 bytes for image data and 32 bytes for 16 color palette entries in A4R4G4B4 format. Depending on the selected graphics mode or the size of the tile-map, there can be as many as 256 HIBs available for tiles and/or sprites.

Tiles are rendered from a tile-map that resides within the extended graphics memory in lieu of a pixel bitmap buffer. Pixel graphics and tile graphics cannot both be active at the same time. Sprites are rendered from a lookup table which shall reside in the last 1024 bytes of the extended graphics buffer.

Graphics Mode Control Registers:

DSP_TMODE (byte read/write): AxBB.BCCC
A = Text Display subsystem enable bit
x = reserved bit
B = Pixel Resolution selection bits (0-7)
C = Color Bit Plane bits (0-7)+1

DSP_GMODE (byte read/write): AxBB.BCCC
A = Pixel Graphics Display subsystem enable bit
x = reserved bit
B = Pixel Resolution selection bits (0-7)
C = Color Bit Plane bits (0-7)+1

Note: Writing to this register will clear ALL previously	allocated display memory blocks. All sprite/tile data will	be invalid and need to be reloaded.

DSP_TIMING_W (word read only): AAAA.AAAA AAAA.AAAA
A = Horizontal Pixel Timing. Default is always 640.

DSP_TIMING_H (word read only): AAAA.AAAA AAAA.AAAA
A = Vertical Pixel Timing. Default is always 400.

DSP_T_WIDTH (byte read only): AAAA.AAAA
A = Columns: Total number of glyphs in text mode, horizontally.

DSP_T_HEIGHT (byte read only): AAAA.AAAA
A = Rows: Total number of glyphs in text mode, vertically.

DSP_T_PITCH (word read/write): AAAA.AAAA AAAA.AAAA
A = Number of GLYPHS displayed horizontally in the text mode.

DSP_T_STRIDE (word/write): AAAA.AAAA AAAA.AAAA
A = Number of GLYPHS per horizontal line in text mode.

DSP_T_PXL_OFS: (read/write) AAAA.BBBB (for smooth scrolling)
A = (signed 4-bit) +/- 8 horizontal pixel offset for text
B = (signed 4-bit) +/- 8 vertical pixel offset for text

DSP_T_START: (read/write) AAAA.AAAA AAAA.AAAA
A = (word) begin rendering text starting with this offset.

DSP_G_WIDTH (byte read only): AAAA.AAAA
A = Columns: Total number of units in gfx mode, horizontally.

DSP_G_HEIGHT (byte read only): AAAA.AAAA
A = Rows: Total number of units in gfx mode, vertically.

DSP_G_PITCH (word read/write): AAAA.AAAA AAAA.AAAA
A = Number of PIXELS displayed horizontally in graphic modes.
DSP_G_STRIDE (word read/write): AAAA.AAAA AAAA.AAAA
A = Number of PIXELS per horizontal line in graphic modes.

DSP_G_PXL_OFS (read/write): AAAA.BBBB (for smooth scrolling)
A = (signed 4-bit) +/- 8 horizontal pixel offset for graphics
B = (signed 4-bit) +/- 8 vertical pixel offset for graphics

DSP_G_START: (read/write) AAAA.AAAA AAAA.AAAA
A = (word) begin rendering pixels starting with this address.

DSP_PAL_INDEX (read/write): AAAA.AAAA
A = Color palette access index.

DSP_PAL_COLOR (word read/write): RRGG.BBAA [DSP_PAL_INDEX]
R = 4-bits of red color data
G = 4-bits of green color data
B = 4-bits of blue color data
A = 4-bits of alpha transparency data

Note: Write to DSP_PAL_COLOR to set the index before reading or	writing color data to/from the 256-color palette array.

DSP_SPR_INDX (read/write): AAAA.AAAA
A = Sprite / Tile data index (0-200)
0 = invalid index or error

DSP_SPR_DATA (320-bytes read/write):
(bytes 0-255) 16x16 256-color indexed pixel bitmap data
(1 byte)	ABCD.Exxx Sprite Control Data
A = visible/enabled
B = collision enable
C = pixel perfect collision enable
D = double horizontal size
E = double vertical size
x = 3 bits reserved
(2 bytes signed)	+/- vertical coordinate
(2 bytes signed)	+/- horizontal coordinate
(? bytes) 4x4 collision mask
(? bytes) up to 25 bytes (200 elements) of collision data
(? bytes) custom user data

DSP_TILE_DATA (320-bytes read/write):
(bytes 0-255) 16x16 256-color indexed pixel bitmap data
(bytes 256-319) custom user data

Emulation Class Object Hierarchy:
Bus	the main loop contains all of the device objects
Device	the base/parent device object
CPU6809	the 6809 emulation layer
Memory	the memory container system
MEM	the parent memory node object
RAM	random access memory (read/write)
ROM	read only memory (read only)
REG	hardware register
Gfx	the graphics container
GfxMode	The graphics mode parent object
GfxPixel	pixel graphics display modes
GfxText	text glyph display modes
GfxCursor	mouse cursor (possibly utilizes GfxSprite)
GfxDebug	a basic debug monitor overlay
GfxTile	the tile graphics modes
GfxSprite	the sprite system
Keyboard	basic keyboard operation
GamePad	gamepad and joystick implementation
Mouse	mouse implementation
Audio	the audio container
AudioMode	The audio mode parent object
AudioDAC	digital to analog audio device (WAV)
AudioFM	frequency modulated audio emulation
GPIO	general input/output pins (parallel)
UART	for headless use/communication
Math	implements random and floating point functions
Timers	implements various hardware timers
FileIO	the file input and output Operating System

Bus
The Bus object acts as a container to dispatch events to all of the
attached devices. After it starts the CPU6809 and Audio threads, it
the main application loop and is responsible for proper device
shutdown as it exits.

Device::
Within the emulation, the Bus object acts as the main device
container, the main loop, and the main event dispatcher. Every device
should inherit from the Device object. The Device object should have
the following virtual members:
OnAttach()	called on creation to add to memory map
OnInit()	calls once after all devices are added
OnQuit()	called when Gfx is closed
OnActivate()	called when opening a new graphics mode
OnDeactivate()	called to close current graphics mode
OnEvent(event)	called when an event was received
OnUpdate(elapsedTime)	called every
OnRender()	called every frame for rendering images

Device::CPU6809
While the 6809 micro-processor will be initially implemented, it	will be possible to implement the Hitachi 6309 in the future by	adding those instructions to the CPU6809 object. In addition to the
inherited member functions, this object should include:
OnClock()	called every clock pulse in its own thread
OnReset()	initiates a reset
OnIRQ()	requests a standard interrupt
OnNMI()	requests a non-maskable interrupt
OnFIRQ()	requests a fast interrupt (video blanking)

Device::Memory	// This is a work in progress
This object handles the memory map and the hardware registers. It	acts as a Memory Node container. In addition to the inherited	members, it should include:
AttachDevice(device, data)	appends device hardware registers
ReadByte(addr, flag)	reads a byte from the memory map
WriteByte(addr, byte)	writes a byte to the memory map
ReadWord(addr, flag)	reads a word from the memory map
WriteWord(addr, word)	writes a word to the memory map
MEM::	the parent memory node object
MEM::RAM	random access memory (read/write)
MEM::	ROM	read only memory (read only)
MEM::	REG	hardware register

Device::Gfx
This object is a container for all of the graphics mode objects. It
receives events from the bus and dispatches them to the GfxMode
objects.

GfxMode::
Defines the parent Graphics Mode object. It implements the following
virtual functions:
OnAttach()	called on creation to add to memory map
OnInit()	calls once after all devices are added
OnQuit()	called when Gfx is closed
OnActivate()	called when opening a new graphics mode
OnDeactivate()	called to close current graphics mode
OnEvent(event)	called when an event was received
OnUpdate(elapsedTime)	called every frame counting elapsed time
OnRender()	called every frame for rendering images

GfxMode::GfxPixel
Implements the pixel graphics modes.

GfxMode::GfxText
Implements the text glyph modes.

GfxMode::GfxCursor
Implements the system cursor. This should also add registers to
customize said cursor. Simply displays a cursor icon at the position	described within the Device::Mouse hardware registers.
GfxMode::GfxDebug
This mode is a simple debug monitor overlay. It should include hex
dumps from multiple addresses that can be modified. It should display
and allow for editing of the registers. It should display a
disassembly of code in memory. Simple assembly functions could also
be implemented. RESET, IRQ, FIRQ, and NMI buttons should also be
present.

GfxMode::GfxTile
This will initially be in a skeleton form. Eventually this class
should implement the tile graphics modes.

GfxMode::GfxSprite
This will initially be in a skeleton form. Eventually this class
should implement the tile graphics modes.

Device::Keyboard
This object dispatches Keyboard events to the Bus for event
distribution. Updates its attached hardware registers.

Device::GamePad
This device object dispatches events from attached gamepads and/or	joysticks to the Bus for event distribution. Updates its own attached	hardware registers.

Device::Mouse
Implements mouse function within its own attached hardware registers.
Dispatches mouse events via the Bus Object.

Device::Audio
Acts as a container for attached AudioMode objects.

AudioMode::
The parent AudioMode object.

AudioMode::AudioDAC
This audio mode object handles two 8-bit digital to analog audio	ports. It should implement simple write to left/right DAC function	directly via hardware register ports. It should also handle clearing,
loading, volume, starting and stopping of WAV files.

AudioMode::AudioFM
This should implement one of the more popular 80’s era FM syntesis
chips. It would be cool to emulate the Commodore 64’s SID chip. Check
it out.

Device::GPIO
Read and/or Write to/from pins. This should dispatch events to the	Bus.

Device::UART
This should implement headless USB/Serial communications to/from	another RETRO_6809 computer or a host Linux/Windows machine.
Device::Math
Includes various 16 and 32 bit floating point operations with	corresponding float to integer conversions. Should implement all of	the most useful half and double precision floating point operations.	Also included in this object should include 16 bit random on read and	the ability to set the random seed on write.

Device::Timers
This should implement registers to read the date, and a 32-bit	“milliseconds since start” counter.
TIMER_DAY	(byte) day of the month (1-31)
TIMER_MONTH	(byte) month (1-12)
TIMER_YEAR	(word) year (0-65535)
TIMER_MS	(dword) number of milliseconds since start

Device::FileIO
This should cover all of the functionality a basic file operating	system should include. Things like, not not limited to, “dir”, “cd”,
“load”, “exec”, etc… should all be covered.

Basic Memory Map:

$0000-$00FF	(256 bytes)	Zero Page: system vectors and variables
$0100-$01FF	(256 bytes)	User Page: low memory user space/stack
$0200-$03FF	(512 bytes)	system stack
$0400-$17FF	(5K bytes)	text display buffer
$1800-$18FF	(256 bytes)	input/output buffer
$1900-$1FFF	(1.75K bytes)	system hardware registers
$2000-$CFFF	(44K bytes)	user RAM space
$D000-$EFFF	(8K bytes)	* paged memory
$F000-$FFEF	(4k bytes)	System KERNEL ROM
$FFF0-$FFFF	(10 bytes)	system hardware vectors

Paged Memory Notes:
bank 0: is simply 8K of fast RAM usable by the system (default)
bank 1: contains the directory structure for persistent memory
banks 2-255: contains 8K pages of persistent memory from 1MB of flash

Bank 0 is always just a 8K bank of fast memory that is usable by the	system for extra RAM for a total of 52K. It can be switched out to	any of the 253 banks	of persistent memory (from TONI’s flash). Bank 1	acts as an allocation	table accessed by ID. That ID is assigned via	the	Kernel. A program can request access to a page of persistent	memory via an assigned ID but it should release that ID when it’s	done using it. This should work similar to new or malloc but	requesting a full 8K page at a time. After use it should be deleted	or freed.

A low level read/write to the memory bank access register can bypass
the allocation function of the KERNEL for direct access. In this case	bank 1 would then be accessible by the program until the KERNEL is	used to once again access the TOC in bank 1 for allocation/releasing.