Retro_6809 Design Document – 24 April 2923

This project is to be an emulated 6809 processor based micro-computer to be developed around a pair of Raspberry PI PICO micro-controllers and a 64k QSPI static RAM chip as an external video buffer. Other chips may be needed to implement USB for mouse, keyboard, and game controllers. Because the older retro style audio chips are no longer in production, FM audio synthesis will be emulated via one of the PICO cores. Graphics will also be emulated using another core. This is to be kind of a “What if?” 80’s style retro computer.

Two Raspberry PI PICO micro-controllers will be used. Each of which has two M0 cores, 260mb RAM, and 2gb flash storage. PICO one, codenamed “TONI”, will drive the 6809 emulation (and 64k mapped memory) and video emulation with its two cores. PICO two, codenamed “KIMI”, will drive both FM synthesis and sampled sound as well as the main event dispatch unit for input and output. A single serial (QSPI) static RAM chip will act as a video buffer for the graphics display modes (or TONI’s graphics buffer).

Text modes will use a short block of internal memory (TONI) for its display buffer. Graphics modes will use the external serial RAM for its buffer. Simple sprite and tile graphics may be implemented in future versions.

TONI:
Core One – 6809 emulation and 64k mapped memory.
This includes implementation of all of the “hardware”

registers within the 6809 addressable memory.
Core Two – Video implementation. This core will render the
text display modes from a block of TONI’s memory, but
will also display the graphics modes that use the
external 64k static memory chip as a buffer. Pixel based
display modes will always display behind the last selected
text modes. Text will be overlayed with alpha transparency.
Sprites and/or tiles may be implemented in the future using
the external ram chip or TONI’s graphics buffer.

KIMI:
Core One – Event dispatch. This core will handle the
dispatching of input/output events such as: Keyboard,
mouse, game-pads, serial ports, GPIO via two USB ports
and/or SPI, QSPI, UART or parallel pins (GPIO).

Core Two – Audio. This core supports both emulated FM
synthesis as well as 8-bit DAC (digital to audio).

64K Quad Serial Static RAM:
Will be used for pixel graphics display information. Display RAM
above what is required for the selected graphics display mode
can be used to define tiles and/or sprites. With optimization,
It may be possible to fit this into TONI’s 260k of memory.
Video Modes:

The text modes include both text glyph based, pixel based, and tile based graphics modes with sprites. Sprites and tile based modes are reserved for future implementation. Graphics modes will use a 16x10 (1.6) aspect ratio with pixel scan rate of 512x320.

Double scan and Quad scan modes in horizontal and/or vertical direction should be implemented. Text glyphs should be based on an 8x8 pixel grid, but 8x12 and 8x16 glyphs might prove to be useful. While ultimately only 12-bits are sent to the digital to analog ladder for display, all display modes are to be palletized into 16-bit (a4 r4 g4 b4) display information. Yes, an alpha channel is to be included for transparent colors. The last text mode will be displayed in front of the graphics mode while utilizing alpha transparency. Both text and graphics are “always on.”

Tile modes and Sprites will likely be implemented later. Their basic
framework should, however, be implemented in skeleton form.

Pixel scan / graphics modes (64k buffer):
Mode:	Res:	1-bpp:	2-bpp:	4-bpp:	8-bpp:
(2 clr)	(4 clr)	(16 clr)	(256 clr)
00	512x320	20480	40960	…	…
01	512x160	10240	20480	40960	…
02	512x80	5120	10240	20480	40960
03	256x320	10240	20480	40960	…
04	256x160	5120	10240	20480	40960
05	256x80	2560	5120	10240	20480
06	128x320	5120	10240	20480	40960
07	128x160	2560	5120	10240	20480
08	128x80	1280	2560	5120	10240

Text glyph modes: (5k buffer)
Mode:	Res:	Mono:	Color:	MonoMem:	ClrMem:
0	64x40	2560	5120	2.5k	5k
1	64x20	1280	2560	1.25k	2.5k
2	32x40	1280	2560	1.25k	2.5k
3	32x20	640	1280	0.625k	1.25k
Graphics Control Registers:
DSP_GMODE (byte):	ABCC.DDEE
A = VSYNC	0:off	1:on
B = gfx_enable	0:off	1:on
C = bit depth	00:1bpp	01:2bpp	10:4bpp	11:8bpp (text00:mono)
D = h_scan	00:1x	01:2x	10:4x	(text: lsb only)
E = v_scan	00:1x	01:2x	10:4x	(text: lsb only)

DSP_EMUFLAGS (byte):	A0BB.BCCC
A=0:WINDOWED 1:FULLSCREEN	(B: Number of Displays, C: Active Display)

DSP_PXLOFS (byte):	AAAA.BBBB
A = horizontal pixel offset (signed 4-bit)
B = vertical pixel offset (signed 4-bit)
Smooth scrolling affects only text modes.

DSP_TBASE (word):	$0400 (default)
Text Glyph Base Address
NOTE: While this can be changed to any valid 16-bit address,
care should be taken to ensure the screen remains within
the text buffer ($0400-$1800).

DSP_GBASE (word):	$0000 (default)
Graphics Base Address (can be used for page swapping)
Note: This is the base address to begin displaying pixel
graphics information within the external serial QSPI RAM.

DSP_GADDR (word):	$0000-$FFFF (16-bit address)
This is the 16-bit address register for the graphics modes.
Write to set or read to retrieve the current register value.

DSP_GDATA (byte):	$00-$FF (8-bit data)
Current pixel data stored at where the address register points.
Can be used for both read and write operations.

DSP_PALETTE (256-words):
This is an array of 256 color data entries in A4R4G4B4 format.
Depending on the color pixel depth colors default to the lower
indenes first. The higher indexed colors are then unused.

DSP_GLYPH (2k-bytes):
This array contains 256x8 text glyph data. Each text glyph is
8 bytes long. Each bit is a single color pixel.

DSP_SPRITE & DSP_TILES (varies):
Sprites and Tiles will not be immediately implemented, but will
utilize unused serial chip RAM.

DSP_TILE_WIDTH, DSP_TILE_PITCH, DSP_TILE_BASE:
Will later be used to determine base offset, map width, and pitch
within the external serial chip RAM (or TONI’s Graphics Buffer).
Emulation Class Object Hierarchy:
Bus	the main loop contains all of the device objects
Device	the base/parent device object
CPU6809	the 6809 emulation layer
Memory	the memory container system
MEM	the parent memory node object
RAM	random access memory (read/write)
ROM	read only memory (read only)
REG	hardware register
Gfx	the graphics container
GfxMode	The graphics mode parent object
GfxPixel	pixel graphics display modes
GfxText	text glyph display modes
GfxCursor	mouse cursor (possibly utilizes GfxSprite)
GfxDebug	a basic debug monitor overlay
GfxTile	the tile graphics modes
GfxSprite	the sprite system
Keyboard	basic keyboard operation
GamePad	gamepad and joystick implementation
Mouse	mouse implementation
Audio	the audio container
AudioMode	The audio mode parent object
AudioDAC	digital to analog audio device (WAV)
AudioFM	frequency modulated audio emulation
GPIO	general input/output pins (parallel)
UART	for headless use/communication
Math	implements random and floating point functions
Timers	implements various timers within the registers
FileIO	the file input and output Operating System

Bus
The Bus object acts as a container to dispatch events to all of the
attached devices. After it starts the CPU6809 and Audio threads, it
the main application loop and is responsible for proper device
shutdown as it exits.

Device::
Within the emulation, the Bus object acts as the main device
container, the main loop, and the main event dispatcher. Every device
should inherit from the Device object. The Device object should have
the following virtual members:
OnAttach()	called on creation to add to memory map
OnInit()	calls once after all devices are added
OnQuit()	called when Gfx is closed
OnActivate()	called when opening a new graphics mode
OnDeactivate()	called to close current graphics mode
OnEvent(event)	called when an event was received
OnUpdate(elapsedTime)	called every
OnRender()	called every frame for rendering images

Device::CPU6809
While the 6809 micro-processor will be initially implemented, it	will be possible to implement the Hitachi 6309 in the future by	adding those instructions to the CPU6809 object. In addition to the
inherited member functions, this object should include:
OnClock()	called every clock pulse in its own thread
OnReset()	initiates a reset
OnIRQ()	requests a standard interrupt
OnNMI()	requests a non-maskable interrupt
OnFIRQ()	requests a fast interrupt (video blanking)

Device::Memory	// This is a work in progress
This object handles the memory map and the hardware registers. It	acts as a Memory Node container. In addition to the inherited	members, it should include:
AttachDevice(device, data)	appends device hardware registers
ReadByte(addr, flag)	reads a byte from the memory map
WriteByte(addr, byte)	writes a byte to the memory map
ReadWord(addr, flag)	reads a word from the memory map
WriteWord(addr, word)	writes a word to the memory map
MEM::	the parent memory node object
MEM::RAM	random access memory (read/write)
MEM::	ROM	read only memory (read only)
MEM::	REG	hardware register

Device::Gfx
This object is a container for all of the graphics mode objects. It
receives events from the bus and dispatches them to the GfxMode
objects.

GfxMode::
Defines the parent Graphics Mode object. It implements the following
virtual functions:
OnAttach()	called on creation to add to memory map
OnInit()	calls once after all devices are added
OnQuit()	called when Gfx is closed
OnActivate()	called when opening a new graphics mode
OnDeactivate()	called to close current graphics mode
OnEvent(event)	called when an event was received
OnUpdate(elapsedTime)	called every frame counting elapsed time
OnRender()	called every frame for rendering images

GfxMode::GfxPixel
Implements the pixel graphics modes.

GfxMode::GfxText
Implements the text glyph modes.

GfxMode::GfxCursor
Implements the system cursor. This should also add registers to
customize said cursor. Simply displays a cursor icon at the position	described within the Device::Mouse hardware registers.
GfxMode::GfxDebug
This mode is a simple debug monitor overlay. It should include hex
dumps from multiple addresses that can be modified. It should display
and allow for editing of the registers. It should display a
disassembly of code in memory. Simple assembly functions could also
be implemented. RESET, IRQ, FIRQ, and NMI buttons should also be
present.

GfxMode::GfxTile
This will initially be in a skeleton form. Eventually this class
should implement the tile graphics modes.

GfxMode::GfxSprite
This will initially be in a skeleton form. Eventually this class
should implement the tile graphics modes.

Device::Keyboard
This object dispatches Keyboard events to the Bus for event
distribution. Updates its attached hardware registers.

Device::GamePad
This device object dispatches events from attached gamepads and/or	joysticks to the Bus for event distribution. Updates its own attached	hardware registers.

Device::Mouse
Implements mouse function within its own attached hardware registers.
Dispatches mouse events via the Bus Object.

Device::Audio
Acts as a container for attached AudioMode objects.

AudioMode::
The parent AudioMode object.

AudioMode::AudioDAC
This audio mode object handles two 8-bit digital to analog audio	ports. It should implement simple write to left/right DAC function	directly via hardware register ports. It should also handle clearing,
loading, volume, starting and stopping of WAV files.

AudioMode::AudioFM
This should implement one of the more popular 80’s era FM syntesis
chips. It would be cool to emulate the Commodore 64’s SID chip. Check
it out.

Device::GPIO
Read and/or Write to/from pins. This should dispatch events to the	Bus.

Device::UART
This should implement headless USB/Serial communications to/from	another RETRO_6809 computer or a host Linux/Windows machine.
Device::Math
Includes various 16 and 32 bit floating point operations with	corresponding float to integer conversions. Should implement all of	the most useful half and double precision floating point operations.	Also included in this object should include 16 bit random on read and	the ability to set the random seed on write.

Device::Timers
This should implement registers to read the date, and a 32-bit	“milliseconds since start” counter.
TIMER_DAY	(byte) day of the month (1-31)
TIMER_MONTH	(byte) month (1-12)
TIMER_YEAR	(word) year (0-65535)
TIMER_MS	(dword) number of milliseconds since start

Device::FileIO
This should cover all of the functionality a basic file operating	system should include. Things like, not not limited to, “dir”, “cd”,
“load”, “exec”, etc… should all be covered.

Basic Memory Map:

$0000-$00FF	(256 bytes)	Zero Page: system vectors and variables
$0100-$01FF	(256 bytes)	User Page: low memory user space/stack
$0200-$03FF	(512 bytes)	system stack
$0400-$17FF	(5K bytes)	text display buffer
$1800-$18FF	(256 bytes)	input/output buffer
$1900-$1FFF	(1.75K bytes)	system hardware registers
$2000-$CFFF	(44K bytes)	user RAM space
$D000-$EFFF	(8K bytes)	* paged memory
$F000-$FFEF	(4k bytes)	System KERNEL ROM
$FFF0-$FFFF	(10 bytes)	system hardware vectors

Paged Memory Notes:
bank 0: is simply 8K of fast RAM usable by the system (default)
bank 1: contains the directory structure for persistent memory
banks 2-255: contains 8K pages of persistent memory from 1MB of flash

Bank 0 is always just a 8K bank of fast memory that is usable by the	system for extra RAM for a total of 52K. It can be switched out to	any of the 253 banks	of persistent memory (from TONI’s flash). Bank 1	acts as an allocation	table accessed by ID. That ID is assigned via	the	Kernel. A program can request access to a page of persistent	memory via an assigned ID but it should release that ID when it’s	done using it. This should work similar to new or malloc but	requesting a full 8K page at a time. After use it should be deleted	or freed.

A low level read/write to the memory bank access register can bypass
the allocation function of the KERNEL for direct access. In this case	bank 1 would then be accessible by the program until the KERNEL is	used to once again access the TOC in bank 1 for allocation/releasing.